## Slide 1: Lab 4: Simple Router
CS144 Lab 4 Screencast
May 2, 2008
Ben Nham
Based on slides by Clay Collier and Martin Casado

## Slide 2: Assignment Overview
You create a virtual network topology, using a topology creation tool
  Covered in intro screencast
You write a router in C
Your router will route real IP packets over the Internet from standard clients (i.e. ping, traceroute, ftp, Firefox…)
Due Wednesday, May 14th before class
  Extended to Saturday, May 17th @ 5:00 PM if you attend class
Get started early!

## Slide 3: Getting Started
Copy the assignment code from: /usr/class/cs144/src/router
Watch the intro screencast to:
  Create a topology
  Create a routing table for the topology
  Compile and run the stub code with a routing table for your topology

## Slide 4: Protocols You Need to Handle
Ethernet
  All packets given to you are raw Ethernet frames
IP
ARP
  Needed to resolve IP addresses to MAC addresses
ICMP requests/replies
  Used by some programs to send requests (ping)
  Needed to send control messages back to host
See sr_protocol.h and Network Sorcery to deal with the raw bits
Make sure you understand your pointer arithmetic!

## Slide 5: Router Basics
myth
elaine
Campus
Network
Your Router
vns-firewall
eth0
eth1
eth2
eth0:
192.168.128.6
eth2:
192.168.129.106
eth1:
192.168.128.50
192.168.128.51
192.168.129.107
ftp 192.168.128.51
192.168.128.51
192.168.128.51
192.168.128.51

## Slide 6: Routing Table
Static routing table in this assignment
Make sure you understand LPM (Section 3)
Loaded for you from the command line into the router context of type struct sr_instance (sr_router.h)
Entries are a linked list of type struct sr_rt (sr_rt.h)
Walk over the routing table linearly to do a longest prefix match on it
0.0.0.0
255.255.255.255
255.255.255.255
Network Mask
eth0
172.24.74.17
0.0.0.0
eth2
192.168.129.106
192.168.129.106
eth1
192.168.128.51
192.168.128.51
Interface
Next-hop
IP address

## Slide 7: Basic Forwarding Principles
Remove IP datagram from Ethernet frame
  Could also be an ARP payload in Ethernet frame
Inspect the packet’s DA. Assuming the packet is destined for someone else:
  Look up next-hop address by doing a LPM on the routing table using the packet’s DA
    If it does not exist, send ICMP host unreachable
  Decrement TTL, update header checksum
    If TTL <= 1, send ICMP time exceeded
    If checksum invalid, drop
  From next-hop address, determine outgoing interface and next-hop MAC address
    If necessary, send ARP request to determine MAC address
  Encapsulate IP datagram in Ethernet packet
  Forward packet to outgoing interface

## Slide 8: Packets Destined for the Router
If the packet’s DA is destined towards one of our interfaces:
  If it’s an ICMP echo request, generate an ICMP echo reply
  Otherwise if it’s a TCP or UDP packet, generate an ICMP port unreachable (needed for traceroute to work)

## Slide 9: Checksums
IP checksum
  Need to check for all IP packet headers; drop packet if checksum is bad
ICMP checksum
  Need to validate for incoming packets destined for us
  Need to calculate for outgoing packets
  Ignore if forwarding
TCP/UDP checksum
  End-to-end checksum, ignore
  Use in_cksum from Lab 3 to calculate checksums

## Slide 10: Handling ARP
Routing table contains next-hop IPs, but you need both a next-hop IP and and a next-hop MAC address
What you have to do:
  Generate ARP requests and parse ARP replies
  Listen to ARP requests and send ARP replies
  Don’t send a request for each packet; instead, use an ARP cache
  Requests should time out after 5 tries of about 1 second each
  ARP cache entries should time out after about 15 seconds
ARP Cache
…
…
00:e0:81:04:08:9b
172.24.74.130
Ethernet MAC Address
IP address

## Slide 11: ARP Cache Class
We’ve given you an ARP cache class containing
  ARP request queue
  ARP cache
ARP cache entries time out automatically after 15 seconds
ARP request queue written so that it is easy consolidate ARP requests across multiple packets, and enforce the ARP request timeout
See pseudocode in sr_arpcache.h

## Slide 12: Required Functionality
Forwarding packets should work
Handles and generates ARP requests/replies correctly
You can download a file using http and ftp from one of the app servers behind the router
You can traceroute to and through the router
You can ping to and through the router
ICMP host and port unreachable messages are generated correctly
ICMP time exceeded messages are generated correctly
No shortcuts taken (don’t forward a packet to every interface)
Should not crash, even with a malformed packet

## Slide 13: Main Functions and Structures
In sr_router.h:
  struct sr_instance is the context of the router
In sr_router.c:
  sr_handlepacket is called for every packet that goes through the router—you have to fill it out
sr_protocol.h contains convenience structs for accessining fields in packets
sr_if.h contains methods for getting information about the router’s interfaces
ARP Cache in sr_arpcache.h

## Slide 14: Suggestions
Think before coding—there’s a good amount of code to write
Don’t put everything in one file, if you want to be able to navigate your code
Read through the Network Sorcery pages to understand the protocols
Read the FAQ
Post and check the newsgroup
Start early

## Slide 15: Demo
Look at working solution