## Slide 1: Delays and IPC
CS144 Review Session 2
April 11, 2008
Ben Nham

## Slide 2: Announcements
Except for things that pertain only to you, use the newsgroup, not the staff list

## Slide 3: Delays
We want to send a message between two hosts, hooked up directly via a link
  Message is of length L bits
  Link’s transmission rate is R bits per second
  Hosts are distance d meters apart
What are the relevant delays?
  Propagation delay
  Transmission delay
A
B
R bps
d m
L bits

## Slide 4: Propagation Delay
The time it takes to send one bit from A to B
Bounded by:
  Length d of link
  Propagation speed s of link
    Bounded by speed of light
    Usually about 2*108 m/s
Prop delay = d/s
A
B
R bps
d m
L bits

## Slide 5: Transmission Delay
Time it takes for all bits of the message to be pushed onto the link
Bounded by:
  Length L of message
  Transmission rate R of link
    E.g. fully utilized Fast Ethernet = 100 Mbps
    ADSL = 1.5 Mbps (varies)
Transmission delay = L/R
A
B
R bps
d m
L bits

## Slide 6: Total Delay
For one link:
  Total Delay = Prop delay + Trans delay
  = d/s + L/R
  Suppose:
    d = 1 km, s = 2*108 m/s → tprop= 5 μs
    L = 500 bytes, R = 100 Mbps → ttrans = 40 μs
    Total = tprop+ ttrans = 45 μs
What happens when we compose links, placing routers in between?
  Have to add a queuing delay component
A
B
R bps
d m
L bits

## Slide 7: Worst-Case Bisection Bandwidth
Take a network topology, and partition the nodes in two equal parts
Bisection bandwidth = bandwidth of links that travel across partition
The worst possible bandwidth between all sets of equal partitions is the worst-case bisection bandwidth
Note: people commonly use “bisection BW” to mean “worst-case bisection BW”
10 Mbps
100 Mbps
1 Gbps

## Slide 8: Worst-Case Bisection Bandwidth
Take a network topology, and partition the nodes in two equal parts
Bisection bandwidth = bandwidth of links that travel across partition
The worst possible bandwidth between all sets of equal partitions is the worst-case bisection bandwidth
Note: people commonly use “bisection BW” to mean “worst-case bisection BW”
Bisection BW = 40 Mbps
10 Mbps
100 Mbps
1 Gbps

## Slide 9: Client-Server File Transfer
Suppose Blizzard wants to distribute a patch for WoW
  Patch size is 450 MB = 3600 Mbits
  Need to distribute patch to 5 million players over 5 hours
  How many 100 MBps servers are needed?
3600 Mbits * 5 million / 5 hours = 1*1012 bps
1*1012 bps / 100 Mbps = 10000 servers

## Slide 10: Peer to Peer File Transfer
Use one 100 Mbps server, and suppose each client has a 1Mbps full-duplex link
Split the patch into 450 chunks, 1MB each
Then:
  Seed each chunk to one client each
  Wait for every client to get at least one chunk
  Wait for every client to acquire the other 449 chunks

## Slide 11: Seeding
Seed each chunk to one client each
450 * 1 MB / 100 Mbps = 1 min to seed
Server
100 Mbps

## Slide 12: Exponential Growth
Wait for every client to get at least one chunk
We have 450 seed clients with 1 Mbps links
  5 million clients / 450 seeds = 11112 clients/seed
  This distribution takes place exponentially:
    ceil(log2 11112) = 14 time steps
    Each time step is 1 MB / 1 Mbps = 8 s
    Total time: 14 * 8 s = 2 minutes
A
A
B

## Slide 13: Exponential Growth
Wait for every client to get at least one chunk
We have 450 seed clients with 1 Mbps links
  5 million clients / 450 seeds = 11112 clients/seed
  This distribution takes place exponentially:
    ceil(log2 11112) = 14 time steps
    Each time step is 1 MB / 1 Mbps = 8 s
    Total time: 14 * 8 s = 2 minutes
A
A
B
C
D
A
B

## Slide 14: Exponential Growth
Wait for every client to get at least one chunk
We have 450 seed clients with 1 Mbps links
  5 million clients / 450 seeds = 11112 clients/seed
  This distribution takes place exponentially:
    ceil(log2 11112) = 14 time steps
    Each time step is 1 MB / 1 Mbps = 8 s
    Total time: 14 * 8 s = 2 minutes
A
A
B
C
D
A
B
G
H
E
F
C
D
A
B

## Slide 15: Peak Transfer
Now each client has a single chunk
Everyone can utilize their full 1Mbps connection
For any client, takes 449 * 8s = 1 hour to download the rest of the chunks in the patch
Adding up:
  Seeding takes 1 minute
  Exponential growth until everyone has a chunk takes 2 min
  Finishing transfer takes 1 hour
  1 min + 2 min + 1 hour << 5 hours
  1 server << 10000 servers

## Slide 16: Lab 2: Fingerd
Finger service isn’t enabled locally on cluster, so use “finger user@whois.stanford.edu” instead
You will need to understand:
  Writing servers (last week)
  New IPC syscalls:
    fork()
    exec*(…)
    pipe()
    dup2(src, target)

## Slide 17: Forking
Makes a copy of the current process (inherits everything: memory space, file descriptors, signal handlers, …)
The child will return with 0
The parent will return with the pid of the child
Parent must either:
  Explicitly wait on the child
  Install a signal handler that catches the SIGCHLD from child and waits in the signal handler
  Otherwise, zombie process created!
Can use exec* to replace ourselves with another executable
Figure 2-1, The Design and Implementation of 4.4BSD

## Slide 18: Example: Forking Daytime Server
See daytime2.c

## Slide 19: Pipes
A pipe is like a one-way socket
Useful for communicating from parent to child, or vice versa
Bundles two file descriptors together:
  0th can be written to (analogous to stdin)
  1st can be read from (analogous to stdout)
Usual usage for parent to child comm (switch for child to parent comm)
  Create pipe
  Fork
  Parent closes read side of pipe, writes to write side of pipe
  Child closes write side of pipe, reads from read side of pipe

## Slide 20: Duplicating Descriptors
int dup2(intold_desc, intnew_desc)
After execution, new_desc is a copy of old_desc
Example: Sending stdout to stderr
  2 is fd for stderr by default
  1 is fd for stdout by default
  dup2(2, 1)

## Slide 21: Example
Executing the equivalent of "cat /usr/share/dict/words | wc -l"
See numwords.c

## Slide 22: Resources
IPC tutorial on assignment webpage
Man pages
Tutorials:
  Beej’s Guide to Network Programming: http://beej.us/guide/bgnet/
  Beej’s Guide to Unix IPC: http://beej.us/guide/bgipc/