## Slide 1: IP Review
CS144 Review Session 3
April 18, 2008
Ben Nham

## Slide 2: Layering Review
Application |  | Data |  |  | 
↓ |  | ↓ |  |  | 
Transport |  | Data | TCP/UDP Header |  | 
↓ |  | ↓ |  |  | 
Network |  | Data | TCP/UDP Header | IP Header | 
↓ |  | ↓ |  |  | 
Link |  | Data | TCP/UDP Header | IP Header | Ethernet Header

## Slide 3: Characteristics of IP
Connectionless datagram service
  No per-flow state in routers
  Packets may appear out of sequence (successive packets are individually routed)
Unreliable: packets may be dropped
Best-effort: …but only if necessary
A
R1
R2
R4
R3
B
D
H
D
H
Credit: CS244A Handout 4
Source
Destination
Architecture
Links
Topology
Transparent

## Slide 4: Sending IP Packets
Addressing
  Gives endpoints unique names
  Sets of addresses represented by subnets
Forwarding
  Determine the correct egress port for an incoming packet based on a routing table
Routing
  Algorithms to build routing tables in router
  Purpose: choose best path to take from source to dest

## Slide 5: IP Addresses
Every network interface on a host has a globally unique IP address*
32-bit number, usually split into 4 octets:
  128.12.92.1
Grouping IP addresses together is advantageous
  Provides hierarchy
  Consolidates routing table entries
*Ignoring NAT and a few other details we get into later
10000000 | 00001100 | 01011100 | 00000001

## Slide 6: Classful Addressing (Deprecated)
Class A
Class B
Class C
Class D
Class E
1
7
0
Net ID
Host-ID
10
Net ID
Host-ID
24
2
14
16
110
Net ID
Host-ID
3
21
8
1110
Multicast Group ID
4
28
11110
Reserved
5
27
A
127 Networks
B
16k Networks
C
2M
D
0.0.0.0 – 127.255.255.255
128.0.0.0 – 191.255.255.255
192.0.0.0 – 223.255.255.255
224.0.0.0 – 239.255.255.255
240.0.0.0 – 247.255.255.255
0.0.0.0
255.255.255.255
E
Credit: CS244A Handout 4

## Slide 7: CIDR – Classless Inter-Domain Routing
Lets us use variable-length prefixes
  171.64.0.0/14 has room for 256k hosts (2(32-14))
    IP address: 171.64.0.0
    Netmask: 255.252.0.0
  Maps to range: 171.64.0.0 – 171.67.255.255
Try some lookups yourself
  whois -h whois.arin.net 171.64.0.1
  whois -h whois.arin.net 171.68.0.1
11111111 | 11111100 | 00000000 | 00000000
0.0.0.0
255.255.255.255
171.64/14
171.68.0.0
65/8
171.64.0.0
171.67.255.255

## Slide 8: Forwarding
Suppose R1 gets A’s packet
  Does it go out the top or bottom interface?
Resolve by inspecting a routing table
A
R1
R2
R4
R3
B
D
H
D
H
Source
Destination

## Slide 9: Routing Tables
IP Address | Netmask | Gateway | Interface
0.0.0.0 | 0.0.0.0 | 5.10.1.1 | eth0
12.1.0.0 | 255.255.0.0 | 12.1.0.1 | eth1
12.1.1.0 | 255.255.255.0 | 12.1.1.1 | eth2
12.1.1.200 | 255.255.255.255 | 12.1.1.200 | eth3
Matches if: (IPdst & netmask) == (IPtable & netmask)
Can have multiple matches
  12.1.1.200 matches every entry!
  0.0.0.0 entry matches everything (default route)
Each interface has its own IP address
eth0
eth1
eth2
eth3
5.10.1.1
12.1.1.200
12.1.1.1
12.1.0.1

## Slide 10: Longest Prefix Match
IP Address | Netmask | Gateway | Interface
0.0.0.0 | 0.0.0.0 | 5.10.1.1 | eth0
12.1.0.0 | 255.255.0.0 | 12.1.0.1 | eth1
12.1.1.0 | 255.255.255.0 | 12.1.1.1 | eth2
12.1.1.200 | 255.255.255.255 | 12.1.1.200 | eth3
If we have multiple matches, choose entry with longest prefix (largest netmask)
What is the LPM for:
  12.1.1.200
  12.1.0.20
  128.12.92.53
0.0.0.0
255.255.255.255
0.0.0.0/0
12.1.0.0/16
12.1.1.0/24
12.1.1.200/32

## Slide 11: Distance Vectors
Distance vector contains cost to every destination node in the network
For routing, also need next hop to every destination node
Add a cost column to the routing table
  Now routing table is DV: maps Dest IP → (Cost, Next Hop)

## Slide 12: Distributed DV Algorithm (Bellman-Ford)
Initially: only know cost to ourselves and neighbors; everyone else has cost of infinity
Every time we get a distance vector from a neighbor:
  Store neighbor’s distance vector
  For each destination node t in DV:
    Cost to get to t through a neighbor: cost to go to neighbor (in our DV) + cost to go from neighbor to t (in neighbor’s DV)
    Calculate cost to get to t through every neighbor as next hop. The cost to get to t is then the minimum of all these costs
Periodically push our DV to neighbors
  Local routing algorithm: don’t know topology of entire network

## Slide 13: Distance Vector Example
W |  | X |  | Y |  | Z | 
0 | W | ∞ | - | 2 | Y | 1 | Z
x
y
z
2
1
5
w
1
W |  | X |  | Y |  | Z | 
∞ | - | 0 | X | ∞ | - | 1 | Z
W |  | X |  | Y |  | Z | 
2 | W | ∞ | - | 0 | Y | 5 | Z
W |  | X |  | Y |  | Z | 
1 | W | 1 | X | 5 | Y | 0 | Z
W |  | X |  | Y |  | Z | 
0 | W | 2 | Z | 2 | Y | 1 | Z
W |  | X |  | Y |  | Z | 
2 | Z | 0 | X | 6 | Z | 1 | Z
W |  | X |  | Y |  | Z | 
2 | W | 6 | Z | 0 | Y | 3 | W
W |  | X |  | Y |  | Z | 
1 | W | 1 | Z | 3 | W | 0 | Z
W |  | X |  | Y |  | Z | 
0 | W | 2 | Z | 2 | Y | 1 | Z
W |  | X |  | Y |  | Z | 
2 | Z | 0 | X | 4 | Z | 1 | Z
W |  | X |  | Y |  | Z | 
2 | W | 4 | W | 0 | Y | 3 | W
W |  | X |  | Y |  | Z | 
1 | W | 1 | Z | 3 | W | 0 | Z

## Slide 14: Problems with Distance Vector
Increase in link cost is propagated slowly
Can “count to infinity”
  What happens if we delete (B, C)?
  B now tries to get to C through A, and increase its cost to C
  A will see that B’s cost of getting to C increased, and will increase its cost
  Shortest path to C from B and A will keep increasing to infinity
Partial solutions
  Set infinity: set infinity to some finite value
  Split horizon: don’t advertise cost to next hop
  Poison reverse: advertise infinite cost to next hop
A
B
C
2
1

## Slide 15: Dijkstra’s Algorithm
Given a graph G and a starting vertex s, find shortest path from s to any other vertex in G
Use greedy algorithm:
  Maintain a set S of nodes for which we know the shortest path
  On each iteration, grow S by one vertex, choosing shortest path through S to any other node not in S
  If the cost from S to any other node has decreased, update it

## Slide 16: Example
Explored Set S | Unexplored Set Q = V - S
A(0, -) | B(0+2, A), C(∞, -), D(0+9, A), E(∞, -), F(∞, -)
A
B
D
E
C
F
2
1
1
2
9
1
3

## Slide 17: Solution
Explored Set S | Unexplored Set Q = V - S
A(0, -) | B(0+2, A), C(∞, -), D(0+9, A), E(∞, -), F(∞, -)
A(0, -), B(2,A) | C(2+1, B), D(9, A), E(2+3, B), F(∞, -)
A(0, -), B(2, A), C(3, B) | D(9, A), E(5, B), F(3+1, B)
A(0, -), B(2, A), C(3, B), F(4, B) | D(9, A), E(5, B)
A(0, -), B(2, A), C(3, B), F(4, B), E(5, B) | D(5+1, B)
A(0, -), B(2, A), C(3, B), F(4, B), E(5, B), D(6, B) | 
A
B
D
E
C
F
2
1
1
2
9
1
3

## Slide 18: Link-State (Using Dijkstra’s)
Algorithm must know the cost of every link in the network
  Each node broadcasts LS packets to all other nodes
  Contains source node id, costs to all neighbor nodes, TTL, sequence #
  If a link cost changes, must rebroadcast
Calculation for entire network is done locally

## Slide 19: Comparison between LS and DV
Messages
  In distance vector: Each node shares a distance vector (distance to every node in network) with its neighbor
  In link state: Each node broadcasts a link state advertisement to the whole network
How long does it take to converge?
  DV: Varies, can be infinite
  LS: O(|E|2); can be even less if we use a min-heap
Robustness
  DV: An incorrect distance vector can propagate through the whole network, since we are advertising path costs
  LS: we can only incorrectly broadcast cost to neighbors

## Slide 20: Lab 3: Reliable Transport
Half-duplex reliable stream of bytes from client to server
Client reads data from stdin, packetizes data, sends data over network
Server reads data from stdout
Must handle lossy network, corrupted packets, out of order packets w/ buffering (i.e. linked list of packets)
  Sender can only have up to 4 unacked packets outstanding: sender needs state
  Receiver has to handle out of order and missing packets: receiver needs state

## Slide 21: Lab 3 Operation
Client
Server
Data packets
ACK packets
STDIN
STDOUT
Send Buffer
Receive Buffer
handle_pkt
timer
handle_pkt
handle_ack

## Slide 22: Implementation Notes
Takes much more time than Labs 1 and 2, so start early
Define some packet header format to put in front of every packet
  Seq #, Ack #, type (SYN, ACK, …), etc.
For the buffers, probably best to use built-in linked list/stack/queue library
  #include <sys/queue.h>
  Google for manpage
  Tail-queue or doubly-linked list might be useful
Endianness
  Remember htonl/htons and ntohl/ntohs on ints and shorts
  Otherwise your transfer won’t work across different endian machines
Can be selective repeat or Go-Back-N, up to you
  GBN w/ cumulative ACKs is used by TCP and requires less state, so it’s probably easier