## Slide 1: TCP Review
CS144 Review Session 4
April 25, 2008
Ben Nham

## Slide 2: Announcements
Upcoming dates
  Wed, 4/30: Lab 3 due, Lab 4 out
  Fri, 5/2: Midterm Review
  Mon, 5/5: In-class midterm
  Wed, 5/14: Lab 4 due
Lab 3 is more complex than Lab 1 or Lab 2, so start now

## Slide 3: TCP Overview
Network layer protocol
Properties
  Full-duplex connection
    Two-way communication between (IP, port)src and (IP, port)dst
    Connection setup before any transfer
    Connection teardown after transfer finishes
    Each connection creates state in sending and receiving hosts
    How is this different than with a VC network?
  Reliable: resends lost/corrupted segments
  In-order: buffers at sender and receiver
  Stream of bytes: looks like a file you can R/W to

## Slide 4: TCP Segments
URG
ACK
PSH
RST
SYN
FIN
Provide illusion of a stream of bytes, but we actually are going over a datagram network using packets (IP)
Data is carried in TCP segments and placed into an IP packet
Src port
Dst port
Sequence #
Ack Sequence #
HLEN
4
RSVD
6
Window Size
Checksum
Urg Pointer
(TCP Options)
TCP Data
IP Hdr
IP Data
TCP Hdr
TCP Data
15
0
31
Credit: CS244A Handout 8

## Slide 5: Sequence Numbers
Host A
Host B
TCP Data
TCP Data
TCP Hdr
TCP Hdr
ISN (initial sequence number)
Seq number = First byte of segment
Ack seq number = next expected byte
Credit: CS244A Handout 8

## Slide 6: Three-Way Handshake
Exchange initial sequence numbers at connection startup
  Client’s ISN = x
  Server’s ISN = y
Send a special segment with SYN bit set (“synchronize”)
SYN takes up one “byte”
SYN SEQ = x
SYN/ACK SEQ = y, ACK = x+1
ACK = y+1
Client
Server

## Slide 7: Shutdown
Either side can initiate shutdown
Can shutdown only one side of connection, if desired
TIME_WAIT state to handle case of whether last ACK was lost
FIN SEQ = v
ACK ACK = v+1
ACK = w+1
FIN SEQ = w

## Slide 8: Sockets and TCP
connect
send/recv
shutdown (SHUT_RDWR)
shutdown (SHUT_RDWR)
listen
accept
SYN/ACK
SYN
ACK
socket, bind
socket, bind
send/recv
FIN
ACK
FIN
ACK
…

## Slide 9: Sender Window
Window size: maximum amount of unacked bytes/segments
Usually dynamically adjusted in response to congestion
Must be smaller than receiver window
Local state maintained at sender
Window Size
Round Trip Time
Window Size
Sender
Receiver
ACK ACK ACK
Credit: CS244A Handout 8

## Slide 10: Example: Ideal TCP Transfer Rate
Assume an ideal TCP connection between two hosts A and B. What is the maximum transmission rate between the two hosts in terms of:
  W, the window size in bytes
  RTT, the round trip time
  R, the transmission rate of the link

## Slide 11: Solution: Ideal TCP Transfer Rate
Sender
Receiver
ACK
Window Size
Round-Trip Time
(1) RTT > Window Size
ACK
Window Size
RTT
(2) RTT = Window Size
ACK
Window Size
ACK
So ideal transfer rate is W/RTT—independent of link BW!
Credit: CS244A Handout 8

## Slide 12: Receiver Window
Advertised to sender in TCP header
Amount of out-of-order bytes the receiver will buffer
Sender window cannot be larger than advertised receiver window
Example
  RecvWind = receiver window in bytes
  Last ack to sequence number x
  Then receiver will buffer any bytes in the sequence number range [x, x+RecvWind)

## Slide 13: Example: TCP RST Attack
Suppose we have a long-lived TCP connection (like a BGP session), and we want to maliciously terminate it
  Suppose we know the IP and port numbers for both sides of the connection
  Then sending a TCP RST packet will immediately terminate the session
Given a receiver window size of 8K, what is the chance that a RST packet with a random sequence number will terminate the connection?
How many RST packets are needed to span the entire sequence number space?
Using 58 byte RST packets on a 10 Mbps link, how long does it take to generate this number of packets?

## Slide 14: Solution: TCP RST Attack
Given a receiver window size of 8K, what is the chance that a RST packet with a random sequence number will terminate the connection?
  213/232 = 2-19 = 1 in half a million chance
How many RST packets are needed to span the entire sequence number space?
  219 packets
Using 58 byte RST packets on a 10 Mbps link, how long does it take to generate this number of packets?
  219 packets * 58 bytes/packet * 8 bits/byte / 10 Mbps = 24 seconds

## Slide 15: Flow Control
Don’t want to overwhelm the network or the receiver with packets
Adjust cwnd (congestion window) dynamically in response to loss events
  Sender window = min(cwnd, rwnd)
Congestion window resized using AIMD
  When connection starts, start with window size of 1
  As long as segments are acked:
    Increase window size by 1 segment size every RTT (additive increase)
  If loss is detected:
    Halve window size (multiplicative decrease)

## Slide 16: TCP Sawtooth
D
A
D
D
A
A
D
D
A
A
D
A
Src
Dest
t
Window Size
halved
Timeouts
Credit: CS244A Handout 8

## Slide 17: Optimizations
Slow start initialization
  Increase cwnd by MSS for every ack (doubles cwnd for every RTT)
  Suppose we detect first loss at window size W
    Set ssthresh := W/2
    Set cwnd := 1
    Use slow start until our window size is ssthresh
    Then use AIMD (congestion avoidance mode)
Fast retransmit and fast recovery if we get three duplicate acks during slow start
  Suppose we send 1, 2, 3, 4, 5, … , 8, 9, 10
  Get acks 1, 2, 3, 4, 5, …, 8, 8, 8
  Probably 9th segment has been lost, so:
    Resend it before retransmit timer expires (fast retransmit)
    Set cwnd := ssthresh rather than 1 and go into AIMD (fast recovery)

## Slide 18: TCP Sawtooth With Optimizations
halved
Triple-Dup Ack
t
Window Size
Loss
Loss
Slow Start
Slow Start
Credit: CS244A Handout 8

## Slide 19: Example: Reaching Maximum Congestion Window Size with Slow Start
Assume this TCP implementation:
  MSS = 125 bytes
  RTT is fixed at 100 ms (even when buffers start filling)
  Uses slow start with AIMD
  Analyze one flow between A and B, where bottleneck link is 10 Mbps
  Ignore receiver window
What is the maximum congestion window size?
  For one flow (ideally), W/RTT = rate
  W = (100 ms * 10 Mbps) / (8 bits/byte) = 125000 bytes
How long does it take to reach this size?
  Slow start grows cwnd exponentially, starting from one MSS
  Find n s.t. 125 * 2n >= 125000
    n = 10
  Then it takes n * RTT = 1 s to reach the max cwnd size

## Slide 20: Detecting Losses
Each segment sent has a retransmit timer
If a segment’s retransmit timer expires before ack for that segment arrive, assume loss
Retransmission timeout (RTO) for timer based on exponential weighted moving average of the previous RTTs and variance between RTT samples
EstRTTk = (1 − α) · EstRTTk-1 + α · SampleRTTk
  Recommended α is 0.125
  EstRTT is an EWMA of the SampleRTT
DevRTTk = (1 − β ) · DevRTTk-1 + β · |SampleRTTk − EstRTTk|
  Recommended β is 0.25
  DevRTT is an EWMA of the difference between sampled and estimated RTT
RTO = EstRTT + 4 · DevRTT

## Slide 21: Lab 3 Operation
Client
Server
Data packets
ACK packets
STDIN
STDOUT
Send Buffer
Receiver State
handle_pkt
timer
handle_pkt
handle_ack