## Slide 1: Lab 4 and Link Layer
CS144 Review Session 6
May 9, 2008
Ben Nham

## Slide 2: Lab 4 Info
It takes a while, so start now
Watch the first two screencasts to get started
Today: talk about ICMP and ARP for the lab
Due Wednesday, with extension to Saturday at 5 PM

## Slide 3: IP Addresses and MAC Addresses
Each IP address is associated with a single interface
Each interface has a MAC address
Therefore, each IP address is associated with a single MAC address
Router with 4 interfaces has 4 IPs and 4 MAC addresses!
  eth0 has some IP0
  eth1 has some IP1
  eth2 has some IP2
  eth3 has some IP3
Conclusion: An IP address names an interface, not a host
eth0
eth1
eth2
eth3
5.10.1.1
12.1.1.200
12.1.1.1
12.1.0.1
IP1
IP2
IP0
IP3

## Slide 4: IP Within Ethernet
In a router, we operate on raw Ethernet frames, with an IP or ARP packet as payload
To forward a packet one hop, must know:
  Destination IP address
  Next-hop MAC address of the next-hop IP address
Byte 0 | Byte 1 | Byte 2 | Byte 3
Dest MAC Address |  |  | 
Dest MAC Address (continued) |  | Source MAC Address | 
Source MAC Address (continued) |  |  | 
Ethertype |  | Payload | 

## Slide 5: Necessity of ARP
IP Address | Netmask | Gateway | Interface
0.0.0.0 | 0.0.0.0 | 5.10.1.1 | eth0
12.1.0.0 | 255.255.0.0 | 12.1.0.1 | eth1
12.1.1.0 | 255.255.255.0 | 12.1.1.1 | eth2
12.1.1.200 | 255.255.255.255 | 12.1.1.200 | eth3
Suppose I get a packet destined for 128.12.94.3
  Matches default route only (first entry)
Need to send raw Ethernet frame to the MAC address of 5.10.1.1
But our routing table has only IP addresses, not MAC addresses
eth0
eth1
eth2
eth3
5.10.1.1
12.1.1.200
12.1.1.1
12.1.0.1

## Slide 6: ARP Packet Format
Corresponds to struct sr_arphdr
  HTYPE = ar_hrd = htons(ARPHDR_ETHER)
  PTYPE = ar_pro = htons(ETHERTYPE_IP)
  HLEN = ar_hln = # bytes in MAC address
  PLEN = ar_pln = # bytes in IP address
  OPER = ar_op = htons(ARP_REQUEST) or htons(ARP_REPLY)
  SHA/SPA = sender MAC/IP address (copy from sr_if of outgoing IF)
  THA/TPA = target MAC/IP address

## Slide 7: Generating ARP Request
Request: Who has IP 192.168.1.3? Create ARP request with fields:
  Source HW addr: MACsrc
  Source protocol addr: IPsrc
  Target HW addr: all 0s
  Target protocol addr: 192.168.1.3
ARP requests are sent to the Ethernet broadcast address

## Slide 8: Handling ARP Request
Get request: Who has 192.168.1.3
If one of the IPs of my router is 192.168.1.3, send an ARP reply: I have IP of 192.168.1.3 with MAC address of 00-11-22-33-44-55-66 (six bytes in hex, or 48 bits)
  Source HW addr: 00-11-22-33-44-55-66
  Source protocol address: 192.168.1.3
  Target HW addr: MACsrc
  Target protocol addr: IPsrc
ARP reply is sent directly to MACsrc

## Slide 9: Handling ARP Reply
Reply: I have IP of 192.168.1.3 with MAC address of 00-11-22-33-44-55-66
If the target IP of the ARP reply is the IP of the interface this came in on:
  Add the IP to MAC mapping to the ARP cache
  Send off any packets that were waiting on this ARP reply

## Slide 10: Lab 4 ARP Functionality
Generate ARP requests if a next hop MAC is not in the ARP cache
Process ARP replies that target us and place them into the ARP cache
Process ARP requests that target us and generate an appropriate ARP reply
Go through ARP request queue every second and send off ARP requests every second (edit sr_arpcache_sweepreqs in sr_arpcache.c)

## Slide 11: ICMP
Used to send control messages back to sending host
Must process ICMP Echo Request
Must generate
  ICMP Echo Reply
  ICMP Destination Host Unreachable
  ICMP Destination Port Unreachable
Check Network Sorcery pages on details of how to generate the message

## Slide 12: Basic Lab 4 Flow Diagram
Receive Raw Ethernet Frame
Process IP Packet
Process Packet Sent to Self
Forward Packet
Process ARP Request/Reply
If ICMP echo req, send ICMP echo reply
If IP+TCP/UDP, send ICMP port unreachable
Do LPM on routing table
See previous slides
Send ICMP host unreachable
Check ARP cache
Send frame to next hop
Add request to ARP queue, sending if necessary
No match
If already sent 5 times
Match
No hit
Hit
Not sent to self
Sent to self

## Slide 13: More Lab 4 Thoughts
Organize your code
  Sticking everything sr_router.c will probably give you a headache
  Make some new files (suggestions):
    sr_arp.c/h for handling/generating ARP packets
    sr_icmp.c/h for handling/generating ICMP packets
    sr_ip.c/h for to handle generating IP packets
    Add the sources and headers to the Makefile
Do one thing at a time
  Need ARP to send anything at all
  If you just do the forwarding path without ICMP, should be able to route packets to the app servers
  Can add ICMP support last

## Slide 14: MAC Address Uniqueness
IPs should be globally unique across all hosts
  Except for multicast IPs and private IPs used by NATs
MAC addresses only have to be locally unique
  If a node is directly connected to other nodes over a shared Ethernet (or switched/hubbed Ethernet), MAC addresses on this shared medium must be unique or we couldn’t address a frame to just one frame
  But two nodes on opposite sides of the world don’t need unique MAC addresses, since as we’ve seen we’re only using the MAC address to forward the frame one hop
  Network cards come from the factory with a unique MAC address anyway, but users can set their MAC address in software, so duplicate MACs can occur

## Slide 15: Arbitration of Shared Resources
General systems problem
  I have a shared resource that only one person can use at a time
  How do I arbitrate access to it?
Shared CPU, multiple processes need it – OS scheduler
Shared radio spectrum, multiple broadcasters – frequency division multiplexing
One Ethernet coax, multiple clients connected to it – CSMA/CD
  Other ways of sharing a medium, e.g. Token Ring, Aloha, etc. in book

## Slide 16: CSMA/CD in the Classroom
We are students sharing the air in this room, and develop the following protocol to arbitrate access to it:
  Before I talk, I see if anyone else is talking
  If anyone else is talking, don’t talk
  If no one else is talking, start talking
  If I start talking and sense that someone else has started talking, stop talking, and start talking some random time that increases exponentially to hope that no one is sending then

## Slide 17: CSMA/CD in Ethernet
We are nodes sharing this Ethernet wire, and develop the following protocol to arbitrate access to it:
  Before I send, I sense the wire to see if anyone else is sending
  If anyone else is sending, don’t send
  If no one else is sending, start sending
  If I start sending and sense that someone else has started sending, stop sending, and start sending after waiting some random time that increases exponentially, to hope that no one is sending then
  This is why CSMA/CD is known as an “exponential backoff” algorithm

## Slide 18: Length Limitation of CSMA/CD
There is a minimum size frame needed to be able to detect collisions:
  Transmission Delay > 2 * Propagation Delay
  Transmission Delay = MinSize / TransferRate
  MinSize = TransferRate * 2 * Propagation Delay
Longer wire = larger prop delay = larger MinSize
Faster transfer rate = larger MinSize
  Serious problem with Gigabit Ethernet and higher
  Punt problem by saying that everyone is using switched networks anyway and not going to get collisions

## Slide 19: CSMA/CD Network Size Restriction
To ensure that a packet is transmitted without a collision, a host must be able to detect a collision before it finishes transmitting a packet.
PROP
PROP
t=0
t=PROP--
t=PROP
t=2PROP-
A
B
Events:
t=0: Host A starts transmitting a packet.
t=PROP--: Just before the first bit reaches Host B, Host B senses the line to be idle and starts to transmit a packet.
t=PROP-: A collision takes place near Host B.
t=PROP: Host B receives data whilst transmitting, and so detects the collision. t=2PROP-: Host A receives data whilst transmitting, and so detects the collision.
“Line is idle”
t=PROP-
“Line is idle”

## Slide 20: Switching vs. Point to Point
Another general systems trend
  Buses are slow, but require less links
  Point to point is fast, but requires more links
  Everything is going from buses to point to point
    Multi-core CPUs: Front Side Bus to HyperTransport
    Hard drives: Parallel ATA to Serial ATA
    Peripheral cards: PCI to PCI Express
    Networking: Shared Ethernet to Switched Ethernet
If we use switching, none of these MAC arbitration protocols matter!

## Slide 21: Manchester Encoding
Synchronous digital systems need a clock to trigger sampling of data
Manchester encoding allows us to encode the clock with the data stream
  The preamble to the Ethernet frame is used to synchronize the sender clock with the receiver clock
In Manchester encoding:
  Transmitter samples data on edge of clock (usually rising edge)
  If we sample a 1, it is encoded by a rising edge
  If we sample a 0, it is encoded by a falling edge

## Slide 22: Manchester Encoding Question
Suppose a 10Mbps NIC sends into a link an infinite stream of zeros using Manchester encoding. The signal emerging from the adapter will have how many transitions per second?
  2 transitions per bit time
  Bit times occur at clock frequency of 10MHz
  Transitions occur at 20 MHz
clk
data
encoding