## Slide 1: Link Layer and Wireless
CS144 Review Session 7
May 16, 2008
Ben Nham

## Slide 2: Routers, Switches, and Hubs
Routers are network layer devices
  Modify IP datagram (decrement TTL)
  Hosts and other routers must be aware of them
Switches and hubs are link layer devices
  Only care about frames, don’t modify IP datagram
  Transparent to network

## Slide 3: Hubs
Operate as a repeater
  Broadcast an incoming frame to all ports, except for the ingress port
  Like having a longer Ethernet cable that all the hosts tap into
  All ports are on single collision domain!
Advantages: simple, restores signal, potentially fast since we don’t have to buffer or examine frame
Disadvantages: poor bandwidth due to collisions

## Slide 4: Hub Question 1
A 10-port hub is connected to 10 hosts using gigabit links. What is the maximum aggregate transfer rate of data flowing through this network?
  All ports are part of the same collision domain--only one device can send at a time
  Therefore, peak bandwidth is one gigabit

## Slide 5: Hub Question 2
Recall that 100Mbps Ethernet restricts cable lengths to 100m. Suppose we want to connect two hosts which are 1000m apart. Can we use 10 100m cables with 9 hubs in series to accomplish this?
  No. Since all ports are on same collision domain, max network diameter (1km) is too large to meet the TRANSP > 2 * PROP constraint of CSMA/CD
  In reality, the IEEE standard limits number of hubs in series and specifies maximum network diameter

## Slide 6: Switches
Must store and examine frame before forwarding
Simple learning protocol—no configuration
  Given incoming frame (MACsrc, MACdst) on port x:
  Add (MACsrc, x) to switch table
  Look up port for MACdst for in switch table
    If entry is there, forward frame to that port
    Else, broadcast frame to all ports (except ingress port)
  Runs spanning tree protocol to prevent loops
Collision domain is a single port—switch will make sure that the frame it sends out does not collide with another frame being sent on the same link

## Slide 7: Memory Mapped Registers
Can send a command to hardware through memory-mapped registers
These addresses aren’t mapped to physical memory, but rather to the HW device
  Store to location writes to HW device over bus
  Load from location reads from HW device over bus

## Slide 8: Direct Memory Access
With memory-mapped registers, CPU is constantly waiting on I/O operations to complete
  I/O devices are usually slower than processors
  Blocks processor
Instead, better to have device write directly to physical memory
This can be done through DMA
  CPU pokes device, goes on to do something else
  Device writes directly to memory
  At some other time (like an interrupt), CPU goes back to fetch data that device wrote to memory

## Slide 9: Polling vs. Interrupts
Polling: CPU periodically checks for data from device
  Inefficient if there’s no data for CPU to process, and higher latency
  Efficient if lots of data to process (batches context switches)
Interrupts: Device interrupts CPU’s current execution, making it jump to an interrupt handler
  Efficient if it doesn’t happen much, and lower latency since we don’t wait for a polling timer to timeout
  Can lead to livelock if too many interrupts (e.g. in network cards that process many packets)

## Slide 10: Lab 5: Dynamic Routing
Implement RIP (distance-vector) in Java
You are given a router that already works, except it doesn’t process RIP packets
  Write RIP packet handling code that modifies routing table
  Simulates the network topology locally (doesn’t route real packets)
References
  Assignment webpage
  Textbook: DV (4.5.2) and RIP (4.6.1)
  RIP Version 2 RFC2453 (although you don’t have to implement all the features)

## Slide 11: Distance Vector Refresher
Distributed, local routing algorithm
Exchange routing tables with neighbors
If we find a better cost path to any destination through our neighbors, update the cost

## Slide 12: Pseudocode
Define:
  Dx(y) = cost from x to y (x’s routing table)
  c(x,y) = link cost of edge (x,y)
while True:
wait until we get a routing table from neighbor v
for each new routing table entry received from v that goes to dest:
entry = lookupRoutingTable(dest)
if c(x,v) + Dv(dest) <= entry.curCost or entry.nextHop is v:
entry.nextHop = v
entry.cost = c(x,v) + Dv(dest)
send routing table to all neighbors if Dx changed
Also have to handle updates if a local link metric is updated or goes up/down

## Slide 13: Basic Code Overview
acceptPacket gets called with a new RIP update packet
  RIPRoutingUpdate contains an ArrayList of RIPRoutingUpdate.Entry (get the ArrayList through getAllEntries() method)
  Get cost to neighbor through getLocalLinkInfoForNextHop
Send a packet using m_ports[PORT_UPDATE_OUT].pushOut(packet)
  Packet is of type IPPacket
  Build by creating a new RoutingTableUpdate, and calling addEntry to it
notifyAlarm() gets called periodically, use it to do periodic tasks
  Decrement TTL of routes learned from others
  Send updates if necessary (if timeout interval has passed, or a route timed out)
Get familiar with Java functions for manipulating IPs, applying netmasks
  Netutils.applyNetMask
  InetAddress class
Use Clack JavaDoc from assignment webpage for reference

## Slide 14: Additional Cases
New network advertised
  Add to routing table
Ignore updates to one of your own prefixes if you know they’re down already
  Otherwise you could end up thinking you have a route to yourself that you know is already down!
Local link metric has updated or local link has gone down
Split horizon with poison reverse
  If I learned a route from you as next hop, I send you infinite as the route cost in the update to you